Porsche 914 Wiper Interval Relay Harness Installation Instructions
For 914 Porsche 1972-76 only

Special thanks to this from SirAndy, Tomeric914, Mark Heard and George Hussey, for this information

“You simply cut the plastic bottom tab off on the switch “

“It is still an easy addition because the intermittent harness plugs in between the main harness and the wiper motor. Just purchase the harness plug it in, add the relay, mount the harness relay stand, and break off the small piece of plastic on the turn switch to enable the wiper switch to move downwards from the off position”

“The picture is a little off. The angle of cover for the ignition switch is in the corner. You just cut the bottom of the plastic tab on the wiper switch. 1st picture show switch with not cut off. You can take a knife and cut tab off with column in car, or you can cut it off smooth be for installing switch.”

A)  The optional equipment Wiper Interval Relay harness

The relay socket mounts with one 6mm bolt/nut to the existing hole on the cowl brace (Fig 1)

The wiper interval relay harness above (Fig. 2), includes a Relay-Socket with 5 female connectors, one in the center, 4 around.  The 5 wires are color coded as follows:
brown/black, blue/black, red, green/white, brown.

The factory manual refers to the wiper interval delay circuit as brown/black wire #91 (see Figs. 3, 4, 5)

B)  Locate the control wire for the relay
The relay control wire is a brown/black wire in the main chassis harness that begins at the steering column (far left connector, first wire, see Fig. 6) and routes in the main harness through the front firewall towards the wiper motor.  The wire terminates around the first support bracket (drivers side, see Fig. 1) near the wiper motor.  The wire is lapped over and taped onto the main harness, just find the lump in the harness under the tape and remove the tape to expose the wire.

C)  Locate the 4 wires on the wiper motor (Fig. 8)
The wiper motor wires are color coded as follows: red/black, green/white, black/blue, black/purple

D)  Insert the relay harness wires in line with the original motor wires (Figs. 7, 9)

1) Remove the red/black wire from the wiper motor. Attach the relay red wire to the motor (it has a double connector) then put the red/black back on the second pin.

2) Remove the green/white wire from the motor and attach it to the relay blue/black wire (male connector, inside the box housing)

3) Take the relay green/white wire and attach it to the previous original green/white connector on the wiper motor

4) Insert the brown/black wire into the only empty connector in the relay socket

5) Attach the relay brown wire to the wiper motor ground

E)  Insert the relay into the relay socket
The original relay, part# 477.955.531

I am told that certain other relays may also work, but have not verified:

111.955.531, 191.955.531, 357.955.531, 321.955.531A, 377.955.531

F)  Now every time you use your windshield washer, the wipers will run for a while, have fun ...

G)  Run it with electric pump
I am told that if you have an electric windshield washer pump, you can also use the (brown/black) control wire to also power your pump, but I have not tried this.  Simply splice the wires and run it to the pump.  See the last diagram.

Fig. 9